## Slide 1: GPS Standard Positioning Service Navigation Solution Software
Patrick Lasagna – Sonal Ranjit

## Slide 2: Project Objective
To get an epoch by epoch least squares position solution of a receiver using its observation and navigation RINEX files.

## Slide 3: What is a RINEX file?
Receiver Independent Exchange Format
Contains raw Satellite observation and navigation data that can be robustly post processed in order to determine an accurate receiver position

## Slide 4: Workflow Diagram
RINEX Observation
File
RINEX
Navigation
File
Reader Class
Observation Dictionary
Navigation Dictionary
Least Squares Filter
SatPos
Receiver ECEF Coordinates and Receiver Clock Error
Run for all Observation Epochs

## Slide 5: RINEX Reader
RINEX files are precisely spaced ascii files that are split into two main parts.
Header
RINEX Body

## Slide 6: Python Dictionary Data Structure
A series of key value pairs, where an alpha-numeric key corresponds to a data value.
“P001”
17.354
17.354
17.354
[“P001”,….. “Pn”]
“Position”
“X Position”
“Y Position”
“Z Position”
“Point Network”
“P001”
“Point List”
“ID”

## Slide 7: RINEX Observation Reader
RINEX Observations are stored on an epoch by epoch basis. Each epoch has several GPS satellites with several pseudorange measurements.
{'07:1:1:0:0:0.0000000': {'EFLAG': '0',
'G06': {'C1': 20857582.237,
'L1': -19771364.963,
'L2': -15406250.872,
'P1': 20857582.016,
'P2': 20857580.516,
'S1': 44.8,
'S2': 40.0},

## Slide 8: RINEX Navigation Reader
RINEX Navigation files are ordered by satellite. Each contain 29 navigation parameters and the epoch they are valid for.
{'G01': {'10:1:1:16:0:0.0': {'Cic': 5.587935447693e-09,
'Cis': 7.636845111847e-08,
'Crc': 183.21875,
'Cuc': -8.651986718178e-06,
...
'Io': 0.9635689853388,
'Mo': 0.0841761497488,
'OMEGA': -0.1005044703918,
'OMEGA_DOT': -7.951402636407e-09,
'Omega': 0.9428572252394,
'SqrtA': 5153.668302536,
'Trans_time': 487788.0},

## Slide 9: Satpos Function
Given an input epoch (and associated navigation parameters), satellite, and pseudorange, determine the position of a satellite.
Determine the closest valid epoch that is less than the input epoch and is no more than two hours away.
Compute the satellite’s position using the navigation data at the correct epoch
If no valid epoch found, ignore this satellite

## Slide 11: Least Squares Filter
  Pseudorange Equation:
  Mathematical Model:
Non-Linear!
Iterative Solution Required Via Taylor’s Theorem!

## Slide 12: Least Squares Solutions

## Slide 13: Results

## Slide 14: DOP Generation
A no nonsense estimator of how good a GPS solution is. Based entirely on satellite geometry and derived from the covariance matrix of the unknowns.

## Slide 15: Geometric DOP
Measure of how good the solution as a whole is

## Slide 17: Position DOP
Measure of how good the position solution is